Aberrations Latin aberrare      "go astray"

→ Thanks to Bret Hess for these viewgraphs

Chromatic Aberration

Problem:  n = n().

Solution: The idea is to use a lens pair with the strongest lens (smallest f) of low dispersion coupled with a weaker one of high dispersion calculated to match the focal lengths for two chosen wavelengths. Cemented doublets “achromats” of this type are a mainstay of lens design.

Spherical Aberration

Problem:  For light rays parallel to the optical axis, at large distances (h) from the axis, small angle approximation breaks down:  f = f(h)

Correction: Restrict h: Aperture or “field stop”.

Correction: Single lens:  vary lens R’s

Example: single: Optimize direction

If you focus a laser beam, or want to form a collimated beam from a focus, and use a plano-convex lens, turn the flat side toward the spherical wavefronts

Correction: Multiple lenses

The 1993 Hubble Telescope repair

HST Repair, cont.

Astigmatism

Problem:  Lens is not completely spherical:  Spherical lens + cylindrical lens:  Rays in different planes have different focal lengths.

Correction:  Add an opposite cylindrical component in a corrective lens

Oblique astigmatism

Problem:  Even if the Lens is spherical, rays from off-axis points in different planes have different focal points, as though the lens were asymmetric: f = f()

Correction:

Spaced doublets with stop.

Aspherical lenses (toroidal components).

Coma

Problem:  For light rays not parallel to the optical axis, rings of different h get focused at different y’s.   f = f(h,)

Get it when your lens is tilted in a beam

→ or (equivalently) when imaging off-axis objects

“Worst aberration”…very asymmetric

Correction: Aperture or field stop

Correction: Single lens: Optimize shape of lens to compromise between minimizing spherical aberr. and coma.  Coma can be made exactly zero for one object distance.

Field curvature

Problem:  Even with other aberrations corrected, planar objects will have different object and image distances for different points, because spherical lenses properly image only curved objects onto curved screens.

Correction:  Multiple lenses

Distortion

Problem:  Magnification may depend on h, even with all other aberrations corrected and everything is focused sharply.

Correction: Multiple lenses, stops

Aperture stops

f-number

Effect of f-number on “depth of view”?

Extreme: Pinhole cameras

Light-gathering ability or “speed” of optical system:

Numerical aperture

for a typical optical system

for immersion microscope

# Text boxes





This lens mainly determines f

This lens mainly corrects dispersion

Not a small angle

Pictures & story from Hecht

Before

After